## Slide 1
Chain Surveying:Chain surveying is a simpllest type of survey in whice is divided into a number of well condition tringles and only linner measurments are ment in the field
When suitable
1.When the sourface is more or less level
2.A small area is to be surveyed
3.A small scale map is to be prepared
4.The formation of well-conditioned triangles is easy
When unsuitable
1.The area is too large
2.The area is consists of too many undulations
3.The area is crowded
4.The formation of well-conditioned triangles is not easy

## Slide 2
Large scale map: when 1cm of a map represent a small distance.it is said to be a large scale map.Having an RF less than 1/500.
Small scale map: when 1 cm of a map represent a large distance.it is said to be a small scale map.Having an Rf more than 1/500.

## Slide 3
Well conditioned triangles
A triangle is called well-conditioned triangle when no angle in it is less than 30 degree or large than 120 degree.
Ill conditioned triangles
A triangle is called ill-conditioned triangle when a angle is less than 30 degree or a angle is large than 120 degree.

## Slide 4
Survey stations
Main stations
Subsidiary stations
Tie stations

## Slide 5
Survey stations
The biggining and the end points of the chain line are called survey stations.
1.Main stations.
which stations are taken along the boundary of an area as controlling points are known as main station.
2.Subsidiary stations.
Which stations are taken on the main survey lines or other chain line are known as subsidiary station.
3.Tie stations.
Which stations are taken on the main survey lines are known as tie stations.

## Slide 6
Base line:The line on which framework of the survey is build is known as base line.
Check line:The line which is used for Checking the accuracy of the triangle is called Check line.
Offsets:Offsets is the lateral shortest distance of an object measured from a survey line.

## Slide 7
Offsets
Parpendicular
offsets
Oblique
offsets

## Slide 8
Perpendicular Offsetes:The parpendicular shortest distance of an object measured from a survey line is called parpendicular offsetes.
Oblique Offsetes:The oblique shortest distance of an object measured from a survey line is called oblique offsetes.

## Slide 9
Ways of taking parpendicular offsets
1.By setting a parpendicular by sawing a tape from the object to the chin line.
2.By setting a right angle in the ratio 3:4:5.
3.By setting a right angle by tri-square.
4.By setting a right angle by optical-square.

## Slide 10
Whey perpendicular offsets are preferred
1.They can be taken very quickly
2.The progress of the survey is not hampered
3.The entry in the field book becomes easy
4.The plotting of the offsets also becomes easy
RUET

## Slide 11
Number of offsets
1.When the boundary of the object is approxiomately parallel to the chain line,parpendicular offsets are taken at regular intervals.

## Slide 12
Number of offsets
2.When the boundary is straight,parpendicular offsets are taken at both ebds of it.

## Slide 13
Number of offsets
When the boundary of the object is circular, parpendicular offsets are taken at regular intervales.

## Slide 14
Number of offsets
When the boundary of the object is zigzag,parpendicular offsets are taken at every bend point.

## Slide 15
Number of offsets
When road cross the chain line parpendicularly,the chainage of the intersection point is to be noted.

## Slide 16
Number of offsets
When the road cross the chain line obliquely,the chainage of the intersection point is to be noted,and at least one parpendicular offset is taken.

## Slide 17
Number of offsets
When the building is small,every corners of the building is fixed by parpendicular or oblique offsets. Other diimension are taken directly at the field.

## Slide 18
Number of offsets
When the building is large,every corners of the building is fixed by parpendicular or oblique offsets.The full plan of the building is drawn in a separet page , and add it at the right place of the field book

## Slide 19
Slection Of Survey Station
1.The base line should be longest of the main survey line.
2.The survey line should be taken through fairly level ground.
3.The main survey line should pass close to the boundary line of the area.
4.The survey line should be close to the object.
5.The survey line should not pass through the main road.
6.The stations should be so selected that the general principle of srveying may be followed.
7.The stations should be intervisible.
8.The stations should be selected in such a way that well conditioned triangles may be formed.
9.Station should be selected in such a way that it avoid chaining obstacle.
10.The tie station should be slected carefully.
11.The subsidiary station should be slectd correctly.

## Slide 20
Equipment For Chain Survey
1.Field book 2.Good pencil
3.Rubber 4.Sharpner
5.Chain 6.Tape
7.Arrows 8.Ranging rods . 9.Offsets Rod 10.Mallet
11.Pages 12.Clinometer
13.Prismatic compass 14.Optical square

## Slide 21
Field Book
The note book in which field measurments are noted is known as the field book.The size of the note book is 20cm×12cm.There are two kinds of field book . 1.Single-line
2.Double-line
Single-line field book:In this type of book,a single red line is drawn through the middle of the each page.The line represent the CHAIN LINE.
Double-line field book:In this type of book, double red line are drawn through the page.This column represent the CHAIN LINE.

## Slide 22
Equipments for plotting
1.Drawing board 2.Tri-square
3.Set-square 4.Protactor
5.Cardboard scale 6.Instrument box
7.French curve 8.Offset scale
9.Dtawing 10.Good pencil
11.Good eraser 12.Board clip
13.Ink 14.Colour
15.Inking pen 16Knife
17.Mini drafter

## Slide 23
Cross-staff: The cross-staff is a simple instrument for setting out right angles.There are three kinds of cross-staff
1.Open
2.French
3.Adjustable
Optical-square:Optical-square is also a instrument for setting out right angles.