## Slide 1
SOURVEYING: sourveying is the art of determining the relative positions of different objects on the sourface of the earth by measuring the horijontal distances between them ,and by preparing a map to any suitable scale.
LEVELING: Leveling is the art of determining the relative positions of different objects on the sourface of the earth by measuring the vertical distances between them ,and by preparing a map to any suitable scale

## Slide 2: USE OF SOURVEYING
1. To prepare a topographical map ,, which shows the hills,valleys,rivers,villages,towns etc
2. To prepare a cadastral map which shows the fields and other properties.
3. To prepare an engineering map which shows the railwayes,roads,cannel etc.
4. To prepare a military map which is very important for the defence of any country.
5. To prepare a contour map which shows the best possible route for railwayes,roads,etc.
6. To prepare a geological map which shows the under ground resources
7. To prepare an archological map which shows the ancient relics

## Slide 3: Classification Of Sourveying
Primary classification
1. Plane sourveying:Plane sourveying is done when the area is lass then 250 square km.
2. Geodetic soueveying:Geodetic soueveying is done when the area is larger then 250 square km.

## Slide 4: Classification Of Sourveying
Secondary Classification
A.BASED ON INUSTRUMENT
1.Chain sourvey
2.Compass sourvey
3.Plane table sourvey
4.Theodolite sourvey
5.Photo graphic sourvey
B.BASED ON METHOD
1.Tringulation sourvey
2.Travers sourvey
C.BASED ON OBJECT
1.Geological sourvey
2.Mine sourvey
4.Arcological sourvey
D.BASED ON NATURE OF FIELD
1.Land sourvey
2.Marine sourvey
3.Astronomical sourvey

## Slide 5
Genaral Principle Of Surveying
1.TO work from the whole to the part.
2.TO locate a new station by at least two measurements ( linear and angular) from fixed reference points.

## Slide 6
METHOD OF LINNEAR MEASURMENT
1.By steeping
2.By passometer
3.By speedometer
4.By chaining
5.By pedometer

## Slide 7: RANGING ROD
RANGING ROD
Ranging rod is a rod which is used for ranging a line.Genarally it is made by timber, bamboo,etc.The colour of the rod is alternative red and white,so that it can be visible from long distance.The lower end of the rod is provided with an iron shoe
Ranging road
Metalic shoe

## Slide 8
TYPE OF CHAIN
ENGINEERING CHAIN:The chain is 100ft long. Number of links is 100 . And each link is 1ft long.
GANDER CHAIN:The chain is 100ft long. Number of links is 100 . And each link is 1ft long
METRIC CHAIN:The chain is long about 5,10,30 ft and length of per link is 25cm
REVENUE CHAIN: The chain is long about 33 ft and length of per link is 33/16 ft

## Slide 9
CHAIN ADVANTAGES
1.The can read easily and quickly
2.The can be easily repaired in the field
CHAIN DISADVANTAGES
1.They take too much time to open and fold
2.The chain sags excessively
STEEL ADVANTAGES
1.They sags slightly
2.They are very easy to open and fold
STEEL DISADVANTAGES
1.They can not read easily and quickly
2.They can not be easily repaired in the field.

## Slide 10
ARROWS
Arrows are made of tempered steel wire of diameter 4mm. One end of the arrow is bent into a ring of diameter 50mm and the other end is pointed. Its overall length is 400mm .Arrows are used for counting the number of chains while neasuring the chain line.
Arrow

## Slide 11
INUSTRUMENT FOR CHAINING
a.Chain or Tape
b.Pegs
c.Offsets rod
d.Plumb bob
e.Arrows
f.Ranging rods

## Slide 12
Type of chain
Folding Chain
Unfolding Chain

## Slide 13
RANGING
The process of establising entermediat points on a straight line betweeen two ends points is knowen as ranging. There are two kinds of ranging.
1.DIRECT RANGING
2.INDIRECT RANGING

## Slide 14
DIRECT RANGING:
The process of establising entermediat points on a straight line betweeen two ends points by direct observation is knowen as DIRECT ranging.
A
B
C
Let A and B are two ends points The two points are intervisible.
Here B is a entermediat point which is establish by the direct
observation of point A and point B. so it is a direct ranging

## Slide 15
INDIRECT RANGING
The process of establising entermediat points on a straight line betweeen two ends points by indirect observation is knowen as INDIRECT ranging.
A
B
C
D
LET A and B are two ends points. These are not intervisible.
Here intermediat points C and D are establising by indirect
Ranging.so it is a example of indirect ranging

## Slide 16
Leader: The chain man at the forward end of the chain, who drages the chain forward, is known as leader
Follower: The chain man at the rear end of the chain,who holds the zero end of the chain at the station, is known as follower.

## Slide 17
METHOD OF CHAINING ON SLOPING GROUND
DIRECT METHOD: this method is applied when the slope of ground is very steep.
INDIRECT METHOD: this method is applied when the slope of ground is very long

## Slide 18
HYPOTENUSAL ALLOWANCE
In this method the slop of the ground is first found out by using clinometer.Hypotenusal allowance than made for each tape length.Let µ is the slope of ground.AB = AB1=20m=100 links
AC=AB secµ
B1C= AC-AB1
= AB secµ-100
=100 ( secµ-1)
B
C
B1
A
µ

## Slide 19
OBSTACLE IN CHAINING
1.When chaining is obostracted but vision is free.
2.When chaining and vision are both obostracted.
3.When chaining is free but vision is obostracted.

## Slide 20
When chaining is obostracted but vision is free.
Souch problem arises when pond or river come across the chain line.The situation is tackled by fllowing wayes.
CASE ONE
When pond come across the chain line.The case is solve by fllowing wayes.
POND
A
B
C
D
E
F
FIG-A
Suppose A and B is a chain line.The two points C and D is selected on it on the two opposite site of the pond.Equal parpendiculars EC and FD is erected on the points C and D. The distance EF is measured. Here CD=EF

## Slide 21
When chaining is obostracted but vision is free.
Souch problem arises when pond or river come across the chain line.The situation is tackled by fllowing wayes.
CASE ONE
When pond come across the chain line.The case is solve by fllowing wayes.
POND
A
B
C
D
E
FIG-B
Suppose A and B is a chain line.The two points C and D is selected on it on the two opposite site of the pond.Equal parpendiculars EC is erected on the points C. IN CED here
ED2 –CE2
CD=

## Slide 22
RIVER
……………………………………………………………..
……………………………………………………………..
……………………………………………………………..
C
F
E
B
A
D
G
CASE TWO
When RIVER come across the chain line.The case is solve by fllowing wayes.
FIG;A
Souppoes AB is the chain line and C,D are the two ends points of the river .At the point of C, CE is erected and bisected at the point of F.A parpenticular EG is erected at the point of E .Points D,F,G should be at same straghit.Here EG is measured and we found here that EG=CD
When chaining is obostracted but vision is free.
Souch problem arises when pond or river come across the chain line.The situation is tackled by fllowing wayes
B

## Slide 23
CASE TWO
When RIVER come across the chain line.The case is solve by fllowing wayes.
RIVER
……………………………………………………………..
……………………………………………………………..
……………………………………………………………..
D
E
G
F
B
A
H
C
FIG:B
When chaining is obostracted but vision is free.
Souch problem arises when pond or river come across the chain line.The situation is tackled by fllowing wayes
Souppoes AB is the chain line and E,D are the two ends points of the river .At the point of D, DF is erected.A parpenticular CG is erected at the point of C .Points E,F,G should be at same straghit.
In the EDF and FGH
HF
HG
DF
DE

## Slide 24
Chaining and vision both are obstacled
Souch problem is arise when building is come across in chain line.The situation is tackled by fllowing ways.
Suppose AB is a chain line .two points C and D are selected at one site of the building .Equal parpenticular CC1 and DD1 is erected.C1D1 is extended until the building is crossed. On the extended line two points E1 and F1 are selected .Then parpendicular
EE1 and FF1 is erected souch a way that EE1=FF1=CC1=DD1
HERE E1D1=ED
E1D1 is measured anf it is equal to required distance ED
BUILDING
E1
A
C1
F1
E
F
B
D1
D
C

## Slide 25
WHEN CHAINING IS FREE BUT VISION IS OBOSTRACTED
Souch problem arises when a rising ground or a jungle area interruptsthe chain line
CASE ONE:The two end stations may be visible from some intermediat points on the rising ground .Here chaining is done by steeping method.
CASE TWO:The two ends points are not visible from intermsdiat points when a jungle come across on the chain line. The case is solve by the fllowing way.
jungle
T
R
E
C1
E1
P
D1
D
C
A
B
Let AB is the actual chain line ,can not visible because of jungle.Let the chain line extenet up to R . A point P is selected on the chain line.And a random line PT is taken . Points C,d,E are taken on the chain line.The parpendicular CC1 meet with the piont C1. The parpendicular DD1 and EE1 meet the point D1 and E1 .Now the distanes PC,PD,PE,CC1 is measured.from triangle PCC1 and PDD1, DD1 is measured.And from traingular PCC1 and PEE1,EE1 is measured.DISTANCE PE1=√(PE₂+EE12)

## Slide 26
Whole circle bearing
In tis system the magnetic bearing of line is measured clockwise from north point up to the line.
W
E
N
S

## Slide 27
Reduced Bearing
In this system the magnetic bearing of a line is measured clockwise from north or south towards east or west
W
E
N
S

## Slide 28
DETERMINE THE HIGHT OF A OBJECT
E
F
D
B
G
C
D
A

## Slide 29
Representative Fraction
Distance on drawing of object
RF = ----------------------------------------------------
Corresponding actual distance of object

## Slide 30
ERRORS OF CHAINING
1.Erroures length of chain or tape
2.Bad ranging
3.Careless holding and marking
4.Bad straighting
5.None horizentaly
6.Sag in chain
7.Variation in temperature
8.Variation in pull
9.Personal mistakes
A .Displacement of arrows
B .Miss counting chain length
C .Miss reading
D .Error lo0king